## Slide 1: Super Mileage Vehicle
Andrew Breier, Anthony Mazzocco, and Blake Pahler
Advisor: Dr. Cho

## Slide 2: Contribution
Team members | System subtask | Weight of contribution
Andy Breier | Script | 100%
Andy Breier | Python code | 40%
Andy Breier | Mock Mount | 10%
Blake Pahler | Python code | 40%
Anthony Mazzocco | Python code | 20%
Anthony Mazzocco | Mock Mount | 90%

## Slide 3: Background
Society of Automotive Engineers club (SAE)
Competition is annual
Every year the vehicle is rebuilt/improved
Change how the driver sees out of vehicle to make it safer and clearer

## Slide 4: Problem
Driver Visibility with current method
  Difficult to see out of sides/front
  Looking between feet to see front
  Material of windows
  Driver gets tested before race
    Usually ends up guessing numbers (unsafe on course)

## Slide 5: Objective
Create a camera system with simple Operating System
Simple user interface
Use camera system so driver can see out of sides and front of car clearly

## Slide 6: Pictures of Current SMV

## Slide 7: Engineering Requirements
Must be able to see objects at least 5ft from the ground
Must be able to see objects at least 20ft in front of vehicle
Must have good resolution (720p or better)
Must be aerodynamic/Low profile cameras
Powered by a battery that is separate from any other power supplies (26,800 mAh USB power bank)
Easily Replaced/Upgraded

## Slide 8: Preliminary Level 0 Design
PowerPower
Camera System
Power
Camera Feed
Surroundings

## Slide 9: Preliminary Level 1 Design
Camera 1
Camera 3
Power
Surroundings
Monitor
Camera Feed
Raspberry Pi4
Power from USB Hub
Camera 2
3.0 USB Hub

## Slide 10: Minicomputer
Raspberry Pi 4
  2x 2.0 USB ports
  2x 3.0 USB ports
  2x micro-HDMI ports
  Can be battery powered
  Uses simple interface

## Slide 11: Cameras
MOKOSE 12MP HDMI/USB Camera
Low profile
Clear Image
Either use USB or HDMI
Field Of View: 85 degrees

## Slide 12: Monitors
Timbrecod 7 inch touchscreen monitor
Includes 3500 mAh Rechargeable battery
Touch Screen
HDMI input

## Slide 13: Alternative Monitor
At least 15.6-inch screen
Each window takes 1/3 of screen
  5.2 inches for each window
USB Powered

## Slide 14: Physical Design Photos

## Slide 15: LXTerminal Script

## Slide 16: Final Output

## Slide 17: Other Possible Output
This way the SMV team has options as to how the cameras look

## Slide 18: Logistical Problem
Budget restricted from acquiring a possible monitor

## Slide 19: Alternative Designs
Three Cameras & 3 Monitors

## Slide 20: Alternative Designs
Two Cameras & 1 Monitor

## Slide 21: Next Steps
Have SMV team test entire system
Implement system into vehicle

## Slide 22: Conclusion
The SAE team works on a Super Mileage Vehicle every year to compete in a competition
The current method to see out of the vehicle can be difficult and unsafe
We are to create a camera system for the vehicle to be able to see the surrounding

## Slide 23: Questions or Comments?